## Slide 1: CSE 4615:: Wireless Networks
Lecture 2
Content Contributors:
Kyle Jamieson and Jennifer Rexford, Princeton University
Volkan Rodoplu, UCSB
Andrea Goldsmith, Princeton University
James F. Kurose and Keith W. Ross, University of Massachusetts Amherst
Christoph Sommer & Falko Dressler, Paderborn University
Overview of Wireless Access Networks
Course Teacher:
Ashraful Alam Khan
Assistant Professor, CSE, IUT

## Slide 2: Internet – the bigger picture
The Internet
Computer Networks
internetworks
Networks
Switches / routers
Communication Links
End systems / hosts

## Slide 3: Protocols and Standards

## Slide 4: The Transport Layer
Multiplexing / de-multiplexing
Reliability & in-order delivery
Congestion control
Flow Control

## Slide 5: The Network Layer
Routing
  Routing Metric
    Hop-count, BW
    ETX, ETT
Routing Protocol
  RIP, OSPF
  BGP
Packet Forwarding
QoS

## Slide 6
A closer look at network structure

## Slide 7: A closer look at network structure:
network edge:
  hosts: clients and servers
  servers often in data centers
physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 8: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks

## Slide 9: Access Networks

## Slide 10: Access Networks
    Nuts and Bolts of Internet

## Slide 11: Access Networks
    End System Interaction

## Slide 12: Access Networks
The network that physically connects an end system to the first router (also known as the “edge router”) on a path from the end system to any other distant end system

## Slide 13: Access Networks Taxonomy based on Technology Used
Access Networks
  Ethernet
  WiFi-Based Access Networks
    Wireless LAN
      802.11a/b/g
    Ad-hoc Networks
      Mesh Networks
      DTN/ICN
      VANET
      6LowPANs
        WSNs
    WiMAX-Based Access Net
    Cellular Networks
      3G Cellular Networks and beyond
    etc…

## Slide 14
Internet
TCP
Ethernet
Wimax based
Low PAN
Wi-Fi based
Cellular Network
IP
Access Networks
Wireless Lan
Mesh Network
ICN/DTN
VANET
WSN
3G Cellular Data Network
Figure: a taxonomy of access networks (approximate)
Access Networks Taxonomy based on Technology Used

## Slide 15
Wired Access Networks
Access Networks

## Slide 16: Access net: digital subscriber line (DSL)
central office
ISP
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  use existing telephone line to central office DSLAM
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
  < 2.5 Mbps upstream transmission rate (typically < 1 Mbps)
  < 24 Mbps downstream transmission rate (typically < 10 Mbps)
DSL
modem
splitter
DSL access
multiplexer

## Slide 17
Cable Network
cable
modem
splitter
…
cable headend
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
frequency division multiplexing: different channels transmitted
in different frequency bands

## Slide 18: Ethernet – Traditional Wired Access

## Slide 19
Wireless Access Networks
Access Networks

## Slide 20: Wireless Access Networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  within building (100 ft)
  802.11b/g (WiFi): 11, 54 Mbps transmission rate
wide-area wireless access
  provided by telco (cellular) operator, 10’s km
  between 1 and 10 Mbps
  3G, 4G: LTE
to Internet
to Internet

## Slide 21: Wireless Access Networks

## Slide 22: Wireless Access Networks: Range Comparison

## Slide 23: Wireless Access Networks

## Slide 24: Milestones in Wireless Communications

## Slide 25: Wireless Networks
Wireless Internet access
Nth generation Cellular
Wireless Ad Hoc Networks
Sensor Networks
Wireless Entertainment
Smart Homes/Spaces
Automated Highways
All this and more…
Ubiquitous Communication Among People and Devices

## Slide 26: Wireless Network: Wireless Link
network
infrastructure
Wireless link
Typically used to connect mobile(s) to base station
Also used as backbone link
Multiple access protocol coordinates link access

## Slide 27: Wireless Network: Wireless Hosts
network
infrastructure
Wireless host
Laptop, PDA, IP phone
Run applications
May be stationary (non-mobile) or mobile

## Slide 28: Wireless Network: Base Station
network
infrastructure
Base station
Typically connected to wired network
Relay responsible for sending packets between wired network and wireless host(s) in its “area”
E.g., cell towers, 802.11 access points

## Slide 29: Wireless Network: Infrastructure
network
infrastructure
Network infrastructure
Larger network with which a wireless host wants to communicate
Typically a wired network
Provides traditional network services
May not always exist

## Slide 30: Wireless Access Networks:: Infrastructure Modes Scenario #1: Infrastructure Mode
network
infrastructure
Infrastructure mode
Base station connects mobiles into wired network
Network provides services (addressing, routing, DNS)
Handoff: mobile changes base station providing connection to wired network
  Client-server communication

## Slide 31
Ad hoc mode
No base stations
Nodes can only transmit to other nodes within link coverage
Nodes self-organize and route among themselves
  Peer-to-peer communication
Wireless Access Networks:: Infrastructure Modes Scenario #2: Infrastructure-less (Ad Hoc) Mode

## Slide 32: Wireless Access Networks:: Infrastructure Modes
 | Infrastructure-based | Infrastructure-less
Single-hop | Base station connected to larger wired network WiFi based wireless LAN Cellular telephony networks WiMAX | One node coordinates the transmissions of the others Bluetooth Ad-hoc 802.11 (e.g., P2P, WiFi Direct)
Multi-hop | Base station exists Some nodes must relay through other nodes Wireless Mesh Networks | No base station exists Some nodes must relay through others Ad hoc wireless Networks Wireless Sensor Networks Mobile Ad-hoc Networks /Vehicular Ad-hoc Networks Delay Tolerant Networks

## Slide 33: Wireless Access Networks:: Infrastructure Modes
 | Infrastructure-based | Infrastructure-less
Single-hop | Base station connected to larger wired network WiFi based wireless LAN Cellular telephony networks WiMAX | One node coordinates the transmissions of the others Bluetooth Ad-hoc 802.11 (e.g., P2P, WiFi Direct)
Multi-hop | Base station exists Some nodes must relay through other nodes Wireless Mesh Networks | No base station exists Some nodes must relay through others Ad hoc wireless Networks Wireless Sensor Networks Mobile Ad-hoc Networks /Vehicular Ad-hoc Networks Delay Tolerant Networks

## Slide 34: Wireless Access Networks:: Infrastructure Modes
 | Infrastructure-based | Infrastructure-less
Single-hop | Base station connected to larger wired network WiFi based wireless LAN Cellular telephony networks WiMAX | One node coordinates the transmissions of the others Bluetooth Ad-hoc 802.11 (e.g., P2P, WiFi Direct)
Multi-hop | Base station exists Some nodes must relay through other nodes Wireless Mesh Networks (semi-structured) | No base station exists Some nodes must relay through others Ad hoc wireless Networks Wireless Sensor Networks Mobile Ad-hoc Networks /Vehicular Ad-hoc Networks Delay Tolerant Networks

## Slide 35: Wireless Access Networks:: Infrastructure Modes
 | Infrastructure-based | Infrastructure-less
Single-hop | Base station connected to larger wired network WiFi based wireless LAN Cellular telephony networks WiMAX | One node coordinates the transmissions of the others Bluetooth Ad-hoc 802.11 (e.g., P2P, WiFi Direct)
Multi-hop | Base station exists Some nodes must relay through other nodes Wireless Mesh Networks (semi-structured) | No base station exists Some nodes must relay through others Ad hoc wireless Networks Wireless Sensor Networks(Structured / Semi-Structured / Un-Structed :: Depending on Application Nature) Mobile Ad-hoc Networks /Vehicular Ad-hoc Networks Delay Tolerant Networks

## Slide 36: Wireless Access Networks
1. Cellular Networks
2. Wireless LANs
3. WiMAX
4. Bluetooth
Single-hop Infrastructure-based
Wireless Systems
Single-hop Infrastructure-less
Wireless Systems
Multi-hop Infrastructure-based
Wireless Systems
Multi-hop Infrastructure-less
Wireless Systems
5. Wireless Mesh Networks (semi-structured)
6. Ad hoc wireless Networks
  6.1. Wireless Sensor Networks (Structured / Semi-Structured / Un-Structed :: Depending on Application Nature)
  6.2. Vehicular Ad-hoc Networks
  6.3. Delay Tolerant Networks

## Slide 37
Single-hop Infrastructure-base
Wireless Access Networks
1. Cellular Networks
2. Wireless LANs
3. WiMAX
Notes: -No backbone: nodes must self-configure into a network.
-In principle all nodes can communicate with all other nodes, but multihop routing can reduce the interference associated with direct transmission.
-Topology dynamic since nodes move around and link characteristics change.
-Applications: appliances and entertainment units in the home, community networks that bypass the Internet. Military networks for robust flexible easily-deployed network (every soldier is a node).

## Slide 38: Single-hop Infrastructure-based:: Cellular Networks
3G cellular data network connects radio access networks to the public Internet.
Figure: 3G cellular data network architecture

## Slide 39: Cellular Networks: Reuse channels to maximize capacity
Geographic region divided into cells
Frequencies/timeslots/codes reused at spatially-separated locations.
Co-channel interference between same color cells.
Base stations/MTSOs coordinate handoff and control functions
Shrinking cell size increases capacity, as well as networking burden
BASE
STATION
MTSO

## Slide 40: Cellular Networks
BS
BS
MTSO
PSTN
MTSO
BS
Santa Barbara
New York
Internet

## Slide 41: Cellular Design: Voice and Data
Data is bursty, whereas voice is continuous
  Typically require different access and routing strategies
3G “widens the data pipe”:
  Standard based on wideband CDMA
  Packet-based switching for both voice and data
Evolution of wireless networks:
    GSM
    IS-95(CDMA)
    CDMA 2000 / W-CDMA // IEEE 802.11a/g/b

## Slide 42: Single-hop Infrastructure-based:: Wireless LANs
Standard | Frequency Range | Data Rate
802.11b | 2.4–2.485 GHz | up to 11 Mbps
802.11a | 5.1–5.8 GHz | up to 54 Mbps
802.11g | 2.4–2.485 GHz | up to 54 Mbps

## Slide 43
WLANs connect “local” computers
Channel access is shared (random access)
Backbone Internet provides best-effort service
01011011
Internet
Access
Point
0101
1011
Single-hop Infrastructure-based:: Wireless LANs

## Slide 44: Single-hop Infrastructure-based:: Wireless LAN Standards
802.11b
  Standard for 2.4GHz ISM band (80 MHz)
  Frequency hopped spread spectrum
  1.6-10 Mbps, 500 ft range
802.11a
  Standard for 5GHz NII band (300 MHz)
  OFDM with time division
  20-70 Mbps, variable range
  Similar to HiperLAN in Europe
802.11g
  Standard in 2.4 GHz and 5 GHz bands
  OFDM
  Speeds up to 54 Mbps

## Slide 45
Data rate :
IEEE 802.11b: 11 Mbps
IEEE 802.11g: 54 Mbps
IEEE 802.11n (Wi-Fi 4): Up to 600 Mbps
IEEE 802.11ac (Wi-Fi 5): Up to 6.9 Gbps
IEEE 802.11ax (Wi-Fi 6/6E): Up to 9.6 Gbps
IEEE 802.11be (Wi-Fi 7) (emerging): Targeting >30 Gbps
Single-hop Infrastructure-based:: Wireless LAN Standards

## Slide 46: (Worldwide Interoperability for Microwave Access)
A wireless communications standard - designed to provide 30 to 40 megabit-per-second data rates, with the 2011 update providing up to 1 Gbit/s for fixed stations.
It refers to interoperable implementations of the IEEE 802.16 family of wireless-networks standards.
Figure: Working Procedure of WiMAX
Single-hop Infrastructure-based:: WiMAX

## Slide 47
Provide portable mobile broadband connectivity across cities and countries
Wireless alternative to cable and digital subscriber line (DSL) for "last mile" broadband access
Provide data, telecommunications (VoIP) and IPTV services (triple play)
A source of Internet connectivity as part of a business continuity plan
Single-hop Infrastructure-based::
WiMAX

## Slide 48
Single-hop Infrastructure-less
Wireless Access Networks
4. Bluetooth
Notes: -No backbone: nodes must self-configure into a network.
-In principle all nodes can communicate with all other nodes, but multihop routing can reduce the interference associated with direct transmission.
-Topology dynamic since nodes move around and link characteristics change.
-Applications: appliances and entertainment units in the home, community networks that bypass the Internet. Military networks for robust flexible easily-deployed network (every soldier is a node).

## Slide 49
8C32810.61-Cimini-7/98
Single-hop Infrastructure-less:: Bluetooth Networks
Master – Slave Communication
only the Master can initiate and control communication within a piconet.
Parked Node: Devices are still synchronized with the master but are not actively participating in communication.
Standby Node: Devices are in an idle state, not connected to any piconet.
Piconet

## Slide 50
Single-hop Infrastructure-less:: Bluetooth Networks
Property | Description
Frequency Band | 2.4 GHz ISM band (2.402 – 2.480 GHz)
Technology | Frequency Hopping Spread Spectrum (FHSS), 1600 hops/sec
Network Topology | Piconet (1 master + up to 7 active slaves)
Data Rate | Up to 721 Kbps (Classic)
Range | ~10 meters (Class 2), up to 100 meters (Class 1)
Roles | Master (initiates & controls communication), Slave (responds to master)
Security | Authentication, Authorization, Encryption
Voice Support | Up to 3 simultaneous SCO voice channels
Device States | Active, Parked, Standby

## Slide 51
Multi-hop Infrastructure-base
Wireless Access Networks
5. Wireless Mesh Networks (semi-structured)
Notes: -No backbone: nodes must self-configure into a network.
-In principle all nodes can communicate with all other nodes, but multihop routing can reduce the interference associated with direct transmission.
-Topology dynamic since nodes move around and link characteristics change.
-Applications: appliances and entertainment units in the home, community networks that bypass the Internet. Military networks for robust flexible easily-deployed network (every soldier is a node).

## Slide 52
Multi-hop Infrastructure-based:: Wireless Mesh Networks

## Slide 53
Multi-hop Infrastructure-based:: Wireless Mesh Networks
Application: Military battlefield communication

## Slide 54
Multi-hop Infrastructure-based:: Wireless Mesh Networks
Application: Maritime Mesh Network

## Slide 55
Multi-hop Infrastructure-based:: Wireless Mesh Networks
Application: Hybrid Wireless Mesh Network for Backbone for Community Broadband Connectivity

## Slide 56
Multi-hop Infrastructure-based:: Wireless Mesh Networks
Application: Drone Mesh Networks (UAV Mesh Networks)

## Slide 57
Multi-hop Infrastructure-based:: Wireless Mesh Networks
Application: Very Large-Scale Agricultural Monitoring with Mobile Machineries

## Slide 58
Multi-hop Infrastructure-based:: Wireless Mesh Networks
Application: Smart & Connected City with Mobile & Static Devices

## Slide 59
1. Network Structure
WMNs consist of two types of devices:
            Mesh Routers (MRs):
          Fixed nodes that form the backbone of the mesh.
          Often connected to the internet.
        Mesh Clients (MCs):
          End-user devices like laptops, phones, sensors.
          Connect to the mesh routers or other clients.
2. Multi-hop Routing
Data travels hop-by-hop through multiple mesh routers to reach its destination.
If a direct path is not available, packets are forwarded through intermediate nodes.
3. Self-Healing Capability
If a node fails or a link breaks, the network automatically reroutes traffic through alternative paths.
Ensures high reliability and robustness.
4. Self-Configuration
New nodes can join the network and start routing without manual configuration.
Each node participates in the routing process and discovers neighbors dynamically.
How WMNs Work
Multi-hop Infrastructure-based:: Wireless Mesh Networks

## Slide 60
Feature | Description
Multi-hop | Increases coverage without requiring all nodes to be in range of each other
Self-healing | Network adapts to failures automatically
Flexible coverage | Nodes can be added easily to expand range
No central controller | Decentralized, peer-based communication
📌 Key Features:
Multi-hop Infrastructure-based:: Wireless Mesh Networks

## Slide 61
📌 Key Challenges:
1. Interference and Shared Medium
Problem: Nodes use a shared wireless medium, leading to co-channel interference, hidden terminal, and exposed terminal problems.
Impact: Reduces throughput and increases collisions.
Multi-hop Infrastructure-based:: Wireless Mesh Networks
2. Scalability
Problem: As the number of nodes increases, routing overhead and contention grow.
Impact: Performance degrades due to increased latency and reduced bandwidth per node.
3. Dynamic Topology & Routing Complexity Problem: Nodes may join, leave, or move, causing frequent route breaks and topology changes.
Impact: Requires adaptive routing protocols and fast convergence.
4. Limited Bandwidth and Throughput
Problem: Each additional hop in a path reduces available bandwidth due to medium reuse.
Impact: End-to-end throughput suffers, especially in large mesh networks.

## Slide 62
📌 Key Challenges:
5. Security Threats
Problem: WMNs are vulnerable to eavesdropping, spoofing, DoS attacks, and routing attacks.
Impact: Compromises confidentiality, integrity, and availability.
Multi-hop Infrastructure-based:: Wireless Mesh Networks
6. Quality of Service (QoS)
Problem: Hard to guarantee latency, jitter, and packet delivery ratio over unreliable, shared wireless links.
Impact: Affects performance of real-time applications like VoIP and video streaming.
7. Synchronization and Coordination
Problem: Distributed nature of WMNs makes scheduling transmissions and synchronizing clocks challenging.
Impact: Causes collisions, inefficient channel use, and poor coordination.
8. Heterogeneity of Devices
Problem: WMNs may include devices with different capabilities, interfaces, and protocols.
Impact: Interoperability issues arise, complicating routing and communication.

## Slide 63
Watch: How do Mesh Networks Works?
Watch: Mesh Networking Idea
Watch: Mesh WiFi Vs. WiFi Extenders
Multi-hop Infrastructure-based:: Wireless Mesh Networks

## Slide 64
Multi-hop Infrastructure-less
Wireless Access Networks
6. Ad hoc wireless Networks
  6.1. Wireless Sensor Networks
  6.2. Mobile Ad-hoc Networks /Vehicular Ad-hoc Networks
  6.3. Delay Tolerant Networks
Notes: -No backbone: nodes must self-configure into a network.
-In principle all nodes can communicate with all other nodes, but multihop routing can reduce the interference associated with direct transmission.
-Topology dynamic since nodes move around and link characteristics change.
-Applications: appliances and entertainment units in the home, community networks that bypass the Internet. Military networks for robust flexible easily-deployed network (every soldier is a node).

## Slide 65
Multi-hop Infrastructure-less:: Wireless Ad-Hoc Networks
Application: Military battlefield communication in Ad-Hoc Mode

## Slide 66
Multi-hop Infrastructure-less:: Wireless Ad-Hoc Networks
Application: Drone Ad-Hoc Networks (UAV Ad-Hoc Networks)
Temporary Internet Coverage
Search and Rescue in Remote Areas
Environmental and Wildlife Monitoring
Disaster Response & Emergency Communications

## Slide 67
Multi-hop Infrastructure-less:: Wireless Ad-Hoc Networks
Application: Search and Rescue & Emergency Communications in Remote Areas

## Slide 68
Multi-hop Infrastructure-less:: Wireless Ad-Hoc Networks
Application: Environmental and Wildlife Monitoring

## Slide 69
Peer-to-peer communications.
No backbone infrastructure.
Routing can be multi-hop.
Topology is dynamic.
Fully connected with different link SINRs
Multi-hop Infrastructure-less:: Ad-Hoc Networks
Notes: -No backbone: nodes must self-configure into a network.
-In principle all nodes can communicate with all other nodes, but multihop routing can reduce the interference associated with direct transmission.
-Topology dynamic since nodes move around and link characteristics change.
-Applications: appliances and entertainment units in the home, community networks that bypass the Internet. Military networks for robust flexible easily-deployed network (every soldier is a node).

## Slide 70
Ad-hoc networks provide a flexible network infrastructure for many emerging applications.
The capacity of such networks is generally unknown.
Transmission, access, and routing strategies for ad-hoc networks are generally ad-hoc.
Cross layer design critical are very challenging.
Energy constraints impose interesting design tradeoffs for communication and networking.
Multi-hop Infrastructure-less:: Ad-Hoc Networks

## Slide 71
Multi-hop Infrastructure-less:: Wireless Mesh Network vs Wireless Ad-Hoc Networks
Aspect | Wireless Mesh Network (WMN) | Wireless Ad-hoc Network (WAHN)
Infrastructure | Semi-infrastructure (uses fixed mesh routers as backbone) | Purely infrastructure-less
Node Roles | Distinct roles: Mesh routers (static) and clients (dynamic) | All nodes are equal; any node can route data
Deployment | Pre-planned, often permanent | Temporary, spontaneous setup
Routing | Stable and optimized (e.g., HWMP, OLSR) | Dynamic and reactive (e.g., AODV, DSR)
Scalability | Highly scalable due to backbone support | Limited scalability due to overhead and congestion
Mobility | Clients may be mobile; routers are often fixed | All nodes may be mobile
Reliability | More reliable due to fixed routers and redundant paths | Less reliable, frequent topology changes
Use Cases | Community networks, smart cities, campus-wide networks | Military ops, disaster relief, emergency response

## Slide 72
Aspect | Wireless Mesh Network (WMN) | Wireless Ad-hoc Network (WAHN)
Radio Interfaces | Often multi-radio and multi-channel (e.g., 802.11s, WiMAX, LTE) | Usually single-radio, single-channel (e.g., 802.11, Bluetooth)
Backhaul Support | Yes, mesh routers may connect to the Internet or backbone | No backhaul, only peer-to-peer communication
Gateway Capability | Mesh routers often serve as gateways to external networks | No defined gateway; all nodes are peers
Energy Source | Often powered (e.g., fixed routers) | Often battery-operated (mobile nodes)
Multi-hop Infrastructure-less:: Wireless Mesh Network vs Wireless Ad-Hoc Networks

## Slide 73
Aspect | Wireless Mesh Network (WMN) | Wireless Ad-hoc Network (WAHN)
Primary Goal | Provide last-mile connectivity and reliable internet access over large areas | Enable peer-to-peer communication in infrastructure-less and mobile environments
Design Focus | Stability, scalability, and long-term connectivity | Quick deployment, flexibility, and dynamic adaptability
Application Focus | Community WiFi, smart cities, industrial IoT, public safety | Military operations, disaster relief, vehicular networks
Traffic Pattern | Typically many-to-one or client-gateway | Dynamic patterns; often all-to-all or many-to-many
Performance Goal | High throughput, fault tolerance, consistent QoS | Fast topology adaptation, minimal delay in dynamic environments
Multi-hop Infrastructure-less:: Wireless Mesh Network vs Wireless Ad-Hoc Networks

## Slide 74
6. Ad hoc wireless Networks
  6.1. Wireless Sensor Networks
  6.2. Mobile Ad-hoc Networks /Vehicular Ad-hoc Networks
  6.3. Delay Tolerant Networks
Feature | WSN | VANET | DTN
Infrastructure-less (or minimal) | ✅ | ✅ | ✅
Multi-hop communication | ✅ | ✅ | ✅
Dynamic topology | ✅ (due to node failure/sleep) | ✅ (due to vehicle mobility) | ✅ (due to intermittent connectivity)
Self-organizing | ✅ | ✅ | ✅
Decentralized control | ✅ | ✅ | ✅
Multi-hop Infrastructure-less:: Wireless Ad-Hoc Networks
Notes: -No backbone: nodes must self-configure into a network.
-In principle all nodes can communicate with all other nodes, but multihop routing can reduce the interference associated with direct transmission.
-Topology dynamic since nodes move around and link characteristics change.
-Applications: appliances and entertainment units in the home, community networks that bypass the Internet. Military networks for robust flexible easily-deployed network (every soldier is a node).

## Slide 75
Wireless Sensor Networks
( Structured / Semi-Structured / Un-Structed :: Depending on Application Nature)
Notes: -No backbone: nodes must self-configure into a network.
-In principle all nodes can communicate with all other nodes, but multihop routing can reduce the interference associated with direct transmission.
-Topology dynamic since nodes move around and link characteristics change.
-Applications: appliances and entertainment units in the home, community networks that bypass the Internet. Military networks for robust flexible easily-deployed network (every soldier is a node).

## Slide 76
  Nodes powered by non rechargeable batteries
  Data flows usually to centralized location.
  Low per-node rates but up to 100,000 nodes.
  Data highly correlated in time and space.
  Nodes can cooperate in transmission, reception, compression, and signal processing.
Energy is the primary constraint
Low power Wireless Sensor Network (Low PAN)[IEEE 802.15]
Multi-hop Infrastructure-less:: Wireless Sensor Networks

## Slide 77: Sensor Networks
Short-range networks must consider transmit, circuit, and processing energy.
  Sophisticated techniques not necessarily energy-efficient.
  Sleep modes save energy but complicate networking.
Changes everything about the network design:
  Delay vs. throughput vs. node/network lifetime tradeoffs.
  Optimization of node cooperation.
Notes: All the sophisticated high-performance communication techniques developed since WW2 may need to be thrown out the window.
By cooperating, nodes can save energy

## Slide 78: Sensor Networks :: Applications

## Slide 79: Sensor Networks :: Applications
Constant monitoring & detection of specific events
Military, battlefield surveillance
Forest fire & flood detection
Habitat exploration of animals
Patient monitoring
Home appliances

## Slide 80: Sensor Networks :: Applications
Precision Agriculture: (Structured / Semi-Structured )
Figure: An example of Low PAN Application

## Slide 81: Military: (Un-Structured )
Remote deployment of sensors for tactical monitoring of enemy troop movements.
Sensor Networks :: Applications

## Slide 82: Smart Home/Smart Office: (Structured)
Sensors controlling appliances and electrical devices in the house
Better lighting and heating in office buildings
Sensor Networks :: Applications

## Slide 83: Medical/Biomedical: Body Area Network: (Structured)
Health Monitors
  Glucose
  Heart rate
  Cancer detection
Chronic Diseases
  Artificial retina
  Cochlear implants
Hospital Sensors
  Monitor vital signs
  Record anomalies
Sensor Networks :: Applications

## Slide 84
Delay/Disruption Tolerant Network (DTN)
(Un-Structed )
Notes: -No backbone: nodes must self-configure into a network.
-In principle all nodes can communicate with all other nodes, but multihop routing can reduce the interference associated with direct transmission.
-Topology dynamic since nodes move around and link characteristics change.
-Applications: appliances and entertainment units in the home, community networks that bypass the Internet. Military networks for robust flexible easily-deployed network (every soldier is a node).

## Slide 85: Interplanetary communication
Delay/Disruption Tolerant Network (DTN)
Notes: Today’s network applications must communicate across totally different networking environments with different link characteristics. Interplanetary Internet that includes both terrestrial and interplanetary links is an extreme case of DTN. Under water marine communication, sensor networks, satellite communication and etc.

## Slide 86: Understanding the TCP and UDP

## Slide 87: TCP, UDP and DTN

## Slide 88: Delay Tolerant Network (DTN)
Figure: Store-And-Forward Message Switching
Figure:

## Slide 89: Delay Tolerant Network
Figure: Store-And-Forward Message Switching
DTN architecture expects nodes to store bundles for an extended period.
Whenever possible, each received data packet is forwarded immediately.
If forwarding is not currently possible but is expected to be possible in the future, the packet is stored for future transmission.

## Slide 90: Delay Tolerant Network
Figure: Store-And-Forward Message Switching
Figure:

## Slide 91: Mobile-enabled delay tolerant networking in rural developing regions
Delay Tolerant Network (DTN):: Applications
Notes: Today’s network applications must communicate across totally different networking environments with different link characteristics. Interplanetary Internet that includes both terrestrial and interplanetary links is an extreme case of DTN. Under water marine communication, sensor networks, satellite communication and etc.

## Slide 92
Delay Tolerant Network (DTN):: Applications
Notes: Application is using mobile computation for real biological research using sensors installed on real zebras.
ZebraNet is a power-aware wireless ad hoc sensor network,
the goal is to use systems to perform novel studies of animal migrations and inter-species interactions.

## Slide 93: ZebraNet (a real life application)
Data
Data
Data
Store-and-forward communications
Data
Tracking node with CPU, FLASH, radio and GPS
First deployment in 2004 in Kenya
Delay Tolerant Network (DTN):: Applications
Notes: Application is using mobile computation for real biological research using sensors installed on real zebras.
ZebraNet is a power-aware wireless ad hoc sensor network,
the goal is to use systems to perform novel studies of animal migrations and inter-species interactions.

## Slide 94: Satellite Systems
Cover very large areas
Different orbit heights
  GEOs (39000 Km) versus LEOs (2000 Km)
Optimized for one-way transmission
  Radio (XM, DAB) and movie (SatTV) broadcasting
Delay Tolerant Network (DTN):: Applications

## Slide 95: DTN :: Characteristics
Internet environment
  End-to-end RTT is not large.
  Some path exists between endpoints.
  E2E reliability using ARQ works well.
  Packet-switching is the right abstraction.
DTN characteristics
  Very large delays.
  Intermittent and scheduled links.
  Different network architectures.
  Conversational protocols fail.
  No ARQ.

## Slide 96
Applications assume e2e ‘connections’
Routing does not understand schedules
Long-term disconnection causes failures
End-to-end reliability is poor with high loss rates
E2E performance is poor with high delays
DTN :: Challenges

## Slide 97
Vehicular Ad-hoc Networks
(Un-Structed )
Notes: -No backbone: nodes must self-configure into a network.
-In principle all nodes can communicate with all other nodes, but multihop routing can reduce the interference associated with direct transmission.
-Topology dynamic since nodes move around and link characteristics change.
-Applications: appliances and entertainment units in the home, community networks that bypass the Internet. Military networks for robust flexible easily-deployed network (every soldier is a node).

## Slide 98: Vehicular Ad-hoc Networks
VANET
a form of Mobile ad-hoc network
provide communication
- among nearby vehicles
- nearby fixed equipment

## Slide 99: Vehicular Ad-hoc Networks
Road-Side infrastructure Units (RSUs), are equipped with on-board processing and wireless communication modules
How vehicular communications work:

## Slide 100
Vehicle-to-Vehicle (V2V)
Vehicle-to-Infrastructure (V2I) communication will be possible
Vehicular Ad-hoc Networks
How vehicular communications work:

## Slide 101: Car-to-X (C2X) Communication Patterns
Vehicle-to-X (V2X)/ Car-to-X (C2X),
Inter-Vehicle Communication (IVC),
Vehicular ad-hoc network (VANET),
…
Illustration: ETSI
… to infrastructure
… to car
… to home

## Slide 102: Car-to-X (C2X) Communication

## Slide 103
Intelligent Transportation Systems (ITS)

## Slide 104
Intelligent Transportation Systems (ITS)

## Slide 105
What can ITS provide ?
Intelligent Transportation Systems (ITS)
Safety
Efficiency
Traffic and road conditions
Road signal alarm
Local information

## Slide 106
Few Emerging Applications that ITS provide ?
Intelligent Transportation Systems (ITS)
Autonomous Intersection Management (AIM)
Vehicle Platooning for Fuel and Space Efficiency
Eco-Driving and Green Routing
Cooperative Perception and Safety Sharing
Autonomous On-Demand Public Transit (Dynamic ride-pooling)
Automated Smart Parking
Real-Time Traffic Prediction and Control
Cooperative Highway Merging and Lane Changing
Dynamic Speed and Lane Recommendations

## Slide 107
Car-to-X (C2X) Communication
Autonomous Intersection Management (AIM):
However, future AIM will adhere Strictly to Fundamental Traffic Rules, Prioritizing Safety as the Top Priority without Human Intervention

## Slide 108
Car-to-X (C2X) Communication
Autonomous Intersection Management (AIM):
Replaces traffic lights with autonomous intersection control, where Connected and Autonomous Vehicles (CAVs) communicate with a central coordinator to avoid collisions.
Research Extensions:
Robustness to Communication Delays and Packet Loss
Human-Driven Vehicle (HDV) and CAV Coexistence Models
Integration with Eco-Driving Strategies
Scalability in High-Density Urban Grids
Benefits:
Minimal vehicle waiting time
Reduced fuel consumption and emissions
Elimination of signal delays
Improved intersection throughput
Enhanced safety

## Slide 109: Cooperative Perception and Safety Sharing Warning!!
Car-to-X (C2X) Communication
What can Car-to-X (C2X) communication provide ?

## Slide 110: Warnings!!! Incident Detection and Reporting
What can Car-to-X (C2X) communication provide ?
Car-to-X (C2X) Communication

## Slide 111: Vehicle Platooning :: Eco-Driving
What can Car-to-X (C2X) communication provide ?
Car-to-X (C2X) Communication

## Slide 112
Vehicle-to-Vehicle (V2V) communication enables direct wireless data exchange between vehicles, allowing them to share real-time information such as position, speed, and braking status.
Vehicle-to-Vehicle (V2V) Communication
Vehicle Platooning:: Eco-Driving
Faster and more synchronized braking response
enhancing safety
enabling closer following distances
improving traffic flow efficiency

## Slide 113
Vehicle-to-Vehicle (V2V) Communication
Depends on human perception and reaction.
Causes significant brake lag and larger following distances.
Manual Driving:
Uses sensors to detect deceleration.
Reduces reaction time but still has processing delays.
Radar-Based Systems:
V2V-Based Platooning:
  Shares braking information wirelessly and instantly.
  Enables simultaneous braking, minimizing brake lag and allowing closer spacing.
Vehicle-to-Vehicle (V2V) communication enhances emergency braking in truck platooning by enabling faster and synchronized braking responses across all vehicles, improving both safety and traffic flow efficiency compared to traditional systems.

## Slide 114: Vehicle Platooning for Improved Fuel Efficiency through Reduced Aerodynamic Drag
What can V2V communication provide ?
Vehicle-to-Vehicle (V2V) Communication

## Slide 115
What can V2V communication provide ?
Vehicle-to-Vehicle (V2V) Communication
Vehicle Platooning for Improved Fuel Efficiency through Reduced Aerodynamic Drag

## Slide 116
Car-to-X (C2X) Communication
Intelligent Traffic Flow Management
What can Car-to-X (C2X) communication provide ?

## Slide 117: Road Traffic Accidents Avoidance
Car-to-X (C2X) Communication
What can Car-to-X (C2X) communication provide ?

## Slide 118: Pedestrian and Cyclist Protection
What can Car-to-X (C2X) communication provide ?
Car-to-X (C2X) Communication

## Slide 119: Car-to-X (C2X) Communication:: Taxonomy of Use Cases
Vehicle-to-X
Non-Safety
Safety
Adaptive Cruise Control
Comfort
Blind Spot Warning
Warning Messages
Electronic Brake Light
Traffic Information Systems
Optimal Speed Advisory
Situation Awareness
Contextual Information
Traffic Light Violation
Entertainment
Congestion, Accident Information

## Slide 120
Non-Safety
Safety
Vehicle-to-X
Many messages
High data rate
Few messages
Small packet size
Low latency demands
Low reliability demands
High latency demands
High reliability demands
Car-to-X (C2X) Communication:: Taxonomy of Use Cases

## Slide 121: Challenges of C2X Communication
Communication
Highly varying channel conditions
Tightly limited channel capacity
Networking
Unidirectional Links
Mobility
Multi-Radio / Multi-Network
But: predictable mobility
Security
No (or no reliable) uplink to central infrastructure
Highly dynamic topology
Heterogeneous equipment
Heterogeneous user base
Ensuring privacy
High congestion, contention, interference
Heterogeneous environment

## Slide 122: Distributed Control over Wireless Links
Packet loss and/or delays impacts controller performance.
Controller design should be robust to network faults.
Joint application and communication network design.
Automated Vehicles
- Cars
- UAVs(Unmanned Aerial Vehicles)
- Insect flyers

## Slide 123
Thank You