## Slide 1: CSE 4615:: Wireless Networks
Lecture 5
Content Contributors:
Kyle Jamieson, Princeton University
Course Teacher:
Ashraful Alam Khan
Assistant Professor, CSE, IUT
Understanding Medium Access Control Mechanisms For Managing Shared Wireless Channels

## Slide 2: Today
How does channel access differ between wireless and wired networks?
Medium access control: Provisioned protocols
Contention-based medium access control

## Slide 3: Wireless is a shared medium
Wired networks:
Alice and Bob’s conversation is independent of Cathy and Eve’s conversation
Wireless networks:
Close by wireless conversations share the same wireless medium
Alice
Bob
Cathy
Eve

## Slide 4: CSMA: Carrier Sense, Multiple Access
Multiple access: channel is shared medium
  Station: wireless host or access point
  Multiple stations may want to transmit at same time
Carrier sense: sense channel before sending
  Station doesn’t send when channel is busy
  To prevent collisions with ongoing transfers
  But, detecting ongoing transfers isn’t always possible
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 5: Collision Avoidance & Collision Detection
Collision detection in wired Ethernet
  Station listens (receives) while transmitting
  Detects collision with other transmission
  Aborts transmission and tries sending again
Problem #1 in Wireless: cannot detect all collisions
  Hidden terminal problem
  Fading
Problem #2 in Wireless: listening while sending
  Strength of received signal is much smaller
  Expensive to build hardware that detects collisions
So, 802.11 does not do collision detection

## Slide 6: Channel Access through CA: Collision Avoidance, Not Detection
Listen to medium and wait until it is free (no one else is talking)
Wait a random backoff time
Advantage: Simple to implement
Disadvantage: Cannot recover from a collision

## Slide 7: Wireless Interference
Two transmitting stations interfere with each other at the receiver
Receiver gets garbage
A
B
C

## Slide 8: Collision Detection and CSMA-CD
Procedure
  Listen to medium and wait until it is free
  Start talking, but listen to see if someone else starts talking too
  If collision, stop; start talking after a random backoff time
Used for hub-based Ethernet
Advantage: More efficient than basic CSMA
Disadvantage: Requires ability to detect collisions by transmitting station.
  Require additional hardware antenna for concurrent receiving while transmitting (Radios are full duplex)
  More difficult in wireless scenario due to significant signal attenuation

## Slide 9: Collision Detection in Wired Network
A
B
C
A’s
C’s signal
strength
Covered Media
C’ s and
A’ s signal
strength
Here, Signal State at Receiver (node B) and Transmitter (Node A) are almost Identical.
‘Fate sharing” of the link’
Hence, Collision Detection at Transmitter (Node A) is Feasible, by sensing(receiving) the signal strength available now by additional receiving antenna while transmission is going on.
Collision experienced at Receiver (node B) while both node A and C are transmitting

## Slide 10: Wireless Link Characteristics
Differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors, microwaves) interfere as well
Wireless is a broadcast medium!
space
Signal Strength
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 11: Wireless Link Characteristics: Attenuation & Propagation range

## Slide 12: Collision Detection in Wireless Network
A
B
C
A’s
C’s signal
strength
Wireless Media
C’ s and
A’ s signal
strength
Here, Signal State at Receiver (node B) and Transmitter (Node A) are NOT Identical.
‘No Fate sharing” of the link’
Hence, Collision Detection at Transmitter (Node A) is NOT Feasible, by sensing(receiving) the signal strength available now by additional receiving antenna while transmission is going on.
Collision experienced at Receiver (node B) while both node A and C are transmitting

## Slide 13: Failure to Detect Collision in Wireless
No “fate sharing” of the link
  High loss rates
  Variable channel conditions
Transmit signal is stronger than received signal
Hence, Cannot take advantage of detecting multiple transmission by simultaneously transmit and receive
Hence, Radios are not full duplex

## Slide 14: Solution: Link-Layer Acknowledgments
Absence of ACK from receiver signals packet loss to sender
Sender interprets packet loss as being caused by collision
Problem: Does not handle hidden terminal cases.
DIFS
Data Transmission
Random
Backoff
ACK Transmission
SIFS

## Slide 15: Carrier Sense Multiple Access with Collision Avoidance (CSMA-CA)
Similar to CSMA but control frames are exchanged instead of data packets
  RTS: request to send
  CTS: clear to send
  DATA: actual packet
  ACK: acknowledgement

## Slide 16: Carrier Sense Multiple Access with Collision Avoidance (CSMA-CA)
Small control frames lessen the cost of collisions (when data is large)
RTS + CTS provide “virtual carrier sense”
    protects against hidden terminal
A
B

## Slide 17: Virtual Carrier Sense
Provided by RTS & CTS
Prevents hidden terminal collisions
A
B
C
RTS
CTS

## Slide 18: Hidden Terminal Revisited
RTS transmission by node A, retrains all the neighbors of A from transmission during A->B transmission.
RTS transmission by node B, retrains all the neighbors of B from transmission during A->B transmission.
A
B
C
RTS
CTS

## Slide 19: Understanding Medium Access: The Problem

## Slide 20: Medium access: The Problem
Receiver must hear ≤1 strong transmission at a time, else collision
(transmissions are lost)
Two questions:
  How should the shared medium be divided?
  Who gets to use each such unit of division, and when?
A medium access control (MAC) protocol specifies the above
Time 🡪
Frequency 🡪

## Slide 21: Today
How does channel access differ between wireless and wired networks?
Medium access control: Provisioned protocols
Contention-based medium access control

## Slide 22: TDMA: Time Division Multiple Access
Channel time is divided into fixed-period, repeating rounds
Each user gets a fixed-length slot (packet time) in each round
  Send across all frequencies during this slot
  Unused slots are wasted
Out-of-band: Mechanism for allocating/de-allocating slots
e.g.: six stations, only 1, 3, and 4 have data to send
6-slot
 | round |  |  |  |  |  |  |  |  |  |  |  | 
 | 1 |  | 3 | 4 |  |  | 1 |  | 3 | 4 |  |  | 
Time

## Slide 23: FDMA: Frequency Division Multiple Access
Channel’s frequency range (for all time) divided into frequency
bands
-Each user gets a fixed frequency band (unused frequency slots are wasted)
e.g.: six stations, only #1, #3, and #4 have data to send
frequency bands 🡪
time 🡪

## Slide 24: TDMA and FDMA: Considerations
Advantages
Users are guaranteed to be able to send bits, continuously (FDMA) or periodically (TDMA)
  Disadvantages
Unused time slots or frequency bands reduce channel utilization
An out-of-band mechanism is needed to allocate slots or bands (which requires another channel). Slot assignment in TDMA isn’t automatic—it requires coordination over a separate signaling channel.
Guard bands or guard times reduce channel utilization

## Slide 25: CDMA: Code Division Multiple Access
All users transmit over the same frequencies, and at the same time:
Allows multiple users to coexist and transmit simultaneously with no interference
Alice (CDMA)
Cathy
Okay!
Bob

## Slide 26: Today
How does channel access differ between wireless and wired networks?
Medium access control: Provisioned protocols
Contention-based medium access control

## Slide 27: Idea: Use a single, shared channel
Spread transmission across whole 100 MHz of spectrum
  Remove constraints assoc. w/one channel per user
    No need for strict one-channel-per-user allocations.
    Users can dynamically access any part of the shared channel, making it more efficient and flexible
  Robust to multi-path fading
    In wireless environments, signals reflect and arrive along multiple paths
    Spreading the signal across many frequencies ensures that even if some parts are lost, others may arrive intact
  Supports peer-to-peer communication
Collisions: Receiver must hear ≤1 strong transmission at a time
So adopt
deference from Ethernet
– Listen (carrier sense, CS) before sending, defer to ongoing

## Slide 28: Concurrency versus Taking Turns
Far-apart links should send concurrently (spatial reuse)
Nearby links should take turns:

## Slide 29: When Does CS Work Well?
Two transmission pairs are far away from each other
– Neither sender carrier-senses the other
AB
CD
B transmits to A, while D transmits to C.

## Slide 30: When Does CS Work Well?
C
B transmits to A, D transmits to C, taking turns.
Both transmitters can carrier sense each other
– Carrier sense uses thresholded correlation value to determine if medium occupied
But what about cases in between these extremes?
AB D

## Slide 31: Hidden Terminal Problem A B C
C can’t hear A, so C will transmit while A transmits – Result: Collision at B
Carrier Sense insufficient to detect all transmissions on wireless networks!
Key insight: Collisions are
spatially located at receiver

## Slide 32: Exposed Terminal Problem A B C
If C transmits, does it cause a collision at A? No!
– Yet C cannot transmit while B transmits to A
Same insight: Collisions spatially located at receiver

## Slide 33: RTS/CTS
Exchange of two short messages: Request to Send (RTS) and
Clear to Send (CTS)
Algorithm
  A sends an RTS (tells B to prepare) with message length k
  B replies an CTS (echoes message length)
  A sends its Data
A
C
1. “RTS, k bits”
3. “Data” B
2. “CTS, k bits”

## Slide 34: Deference to CTS
Hear CTS 🡪 Defer for length of expected data
transmission time
– Solves hidden terminal problem
A
C
1. “RTS, k bits”
3. “Data” B
2. “CTS, k bits”
defers

## Slide 35: Deference to RTS, but not CS
Hear ->RTS ,-> No CTS , -> Data
So terminals
C
Do not transmit to D !
A
C
1. “RTS, k bits”
3. “Data” B
2. “CTS,k bits”
D
But Could transmit to D !

## Slide 36: Deference to RTS, but not CS
exposed
So terminals
B, C
can transmit concurrently:
✅ Common Solutions:
1. RTS/CTS Mechanism (Request to Send / Clear to Send)
  Node B sends an RTS to A.
  A replies with a CTS.
  Node C hears RTS from B but does not hear CTS from A (because A is out of C’s range).
  ➤ C knows it won’t interfere with A and can proceed with its own transmission safely.
✅ Insight: RTS/CTS provides receiver-based collision control, not just sender-based carrier sensing.
A
C
1. “RTS, k bits”
3. “Data” B
2. “CTS,k bits”
D