## Slide 1: CSE 4615:: Wireless Networks
Lecture 1
Content Contributors:
Kyle Jamieson and Jennifer Rexford, Princeton University
Elisabeth Uhlemann, Mälardalens University
Volkan Rodoplu, UCSB
Understanding Wireless Communication: Needs, Barriers, and Design Adaptations
Course Teacher:
Ashraful Alam Khan
Assistant Professor, CSE, IUT

## Slide 2: What You Learn in This Course
How does a Wireless Network Work?
What are the Limitations of Wireless Communications?
How to Address These Limitations to Boost Communication Performance?

## Slide 3: Structure of the Course
Wireless Access Networks
Wireless Communication Fundamental
  Radio Transmission Fundamentals
  Radio Spectrum Regulation
  Communication Requirements
Mesh Networking Basic
Wireless LAN (IEEE 802.11)
VANET (IEEE 802.11p)
Personal Area Network (IEEE 802.15)
Wireless Mobile Network (5g , LTE)
High Throughput (HT) Networks (IEEE 802.11n, MIMO)
Advanced Techniques for Wireless Communication
  Semantic Communication
  ML & AI in Wireless Communications

## Slide 4: Recourses of the Course
Classroom Code: 3tj4qv4w
Invitation Link: https://classroom.google.com/c/Nzc3NjUyNjIwNDE1?cjc=3tj4qv4w
Book Title | Authors
IEEE 802 Wireless Systems, 1st Edition (Wiley) | B. H. Walke, S. Mangold and L. Berlemann
Wireless Communication Networks and Systems by, 1stEd | Beard and Stallings
Wireless Communications, 2nd Edition | Andrea Goldsmith
Wireless Communications and Networks, 2nd Edition | William Stallings

## Slide 5: Fundamentals of Communications
Objective: move a message from point A to point B with the required quality at a minimum cost with respect to certain design criteria
Message: typically, a number of packets or bits
Quality measures
  error probability, e.g., bit or packet or message error rate
  delay: time from when information is available at transmitter until it is output from the receiver
  data rate: number of transmitted bits/second
Resources and costs
  power of transmitted signal (power efficiency)
  bandwidth of transmitted signal (spectral efficiency)
  complexity of transmitter and receiver (hardware and software)
Understanding Wireless Communication:

## Slide 6
How do wireless and wired networks differ?

## Slide 7: Wired Vs. Wireless Communication
Wired | Wireless
Each cable is a different channel
One media (cable) shared by all
Signal attenuation is low
High signal attenuation
High interference
noise; co-channel interference; adjacent channel interference
Low interference (Cross-talk)

## Slide 8: Wired Vs. Wireless Communication
Parameter | Wired Network | Wireless Network
Communication Medium | Copper, Fiber optic | Air (Radio Waves)
Standard | IEEE 802.3 (Ethernet) | IEEE 802.11 family (Wi-Fi)
Mobility & Roaming | Limited | High
Security ? | High (less vulnerable to attacks) | Lower (prone to eavesdropping/hacking)
Speed / Bandwidth | Very High (up to 1 Gbps or more) | Moderate to Low
Delay (Latency) | Low | High
Reliability | Very High | Less reliable
Flexibility to Change | Rigid setup, hard to reconfigure | Highly flexible
Working Principle | CSMA/CD (Collision Detection) | CSMA/CA (Collision Avoidance)
Interference / Fluctuations | Very Low | High (affected by walls, devices, etc.)
Installation Activity | Cumbersome; labor-intensive | Easy; minimal labor
Installation Time | Long (due to cabling, physical setup) | Quick deployment
Connection Type | Usually Dedicated | Shared
Installation Cost | High (cables, labor, devices) | Low
Maintenance Cost | High | Low
Related Equipment | Router, Switch, Hub | Wireless Router, Access Point
Key Benefits | High speed, stable, secure, noise-immune | Cable-free, mobile-friendly, easy to install

## Slide 9: Wired Vs. Wireless Communication
Parameter | Wired Network | Wireless Network
Communication Medium | Copper, Fiber optic | Air (Radio Waves)
Standard | IEEE 802.3 (Ethernet) | IEEE 802.11 family (Wi-Fi)
Mobility & Roaming | Limited | High
Security | High (less vulnerable to attacks) | Lower (prone to eavesdropping/hacking)
Speed / Bandwidth ? | Very High (up to 1 Gbps or more) | Moderate to Low
Delay (Latency) ? | Low | High
Reliability | Very High | Less reliable
Flexibility to Change | Rigid setup, hard to reconfigure | Highly flexible
Working Principle | CSMA/CD (Collision Detection) | CSMA/CA (Collision Avoidance)
Interference / Fluctuations | Very Low | High (affected by walls, devices, etc.)
Installation Activity | Cumbersome; labor-intensive | Easy; minimal labor
Installation Time | Long (due to cabling, physical setup) | Quick deployment
Connection Type | Usually Dedicated | Shared
Installation Cost | High (cables, labor, devices) | Low
Maintenance Cost | High | Low
Related Equipment | Router, Switch, Hub | Wireless Router, Access Point
Key Benefits | High speed, stable, secure, noise-immune | Cable-free, mobile-friendly, easy to install

## Slide 10: Wired Vs. Wireless Communication
Parameter | Wired Network | Wireless Network
Communication Medium | Copper, Fiber optic | Air (Radio Waves)
Standard | IEEE 802.3 (Ethernet) | IEEE 802.11 family (Wi-Fi)
Mobility & Roaming | Limited | High
Security | High (less vulnerable to attacks) | Lower (prone to eavesdropping/hacking)
Speed / Bandwidth | Very High (up to 1 Gbps or more) | Moderate to Low
Delay (Latency) | Low | High
Reliability ? | Very High | Less reliable
Flexibility to Change | Rigid setup, hard to reconfigure | Highly flexible
Working Principle | CSMA/CD (Collision Detection) | CSMA/CA (Collision Avoidance)
Interference / Fluctuations | Very Low | High (affected by walls, devices, etc.)
Installation Activity | Cumbersome; labor-intensive | Easy; minimal labor
Installation Time | Long (due to cabling, physical setup) | Quick deployment
Connection Type | Usually Dedicated | Shared
Installation Cost | High (cables, labor, devices) | Low
Maintenance Cost | High | Low
Related Equipment | Router, Switch, Hub | Wireless Router, Access Point
Key Benefits | High speed, stable, secure, noise-immune | Cable-free, mobile-friendly, easy to install

## Slide 11: Wired Vs. Wireless Communication
Parameter | Wired Network | Wireless Network
Communication Medium | Copper, Fiber optic | Air (Radio Waves)
Standard | IEEE 802.3 (Ethernet) | IEEE 802.11 family (Wi-Fi)
Mobility & Roaming | Limited | High
Security | High (less vulnerable to attacks) | Lower (prone to eavesdropping/hacking)
Speed / Bandwidth | Very High (up to 1 Gbps or more) | Moderate to Low
Delay (Latency) | Low | High
Reliability | Very High | Less reliable
Flexibility to Change ? | Rigid setup, hard to reconfigure | Highly flexible
Working Principle ? | CSMA/CD (Collision Detection) | CSMA/CA (Collision Avoidance)
Interference / Fluctuations | Very Low | High (affected by walls, devices, etc.)
Installation Activity | Cumbersome; labor-intensive | Easy; minimal labor
Installation Time | Long (due to cabling, physical setup) | Quick deployment
Connection Type | Usually Dedicated | Shared
Installation Cost | High (cables, labor, devices) | Low
Maintenance Cost | High | Low
Related Equipment | Router, Switch, Hub | Wireless Router, Access Point
Key Benefits | High speed, stable, secure, noise-immune | Cable-free, mobile-friendly, easy to install

## Slide 12: Wired Vs. Wireless Communication
Parameter | Wired Network | Wireless Network
Communication Medium | Copper, Fiber optic | Air (Radio Waves)
Standard | IEEE 802.3 (Ethernet) | IEEE 802.11 family (Wi-Fi)
Mobility & Roaming | Limited | High
Security | High (less vulnerable to attacks) | Lower (prone to eavesdropping/hacking)
Speed / Bandwidth | Very High (up to 1 Gbps or more) | Moderate to Low
Delay (Latency) | Low | High
Reliability | Very High | Less reliable
Flexibility to Change | Rigid setup, hard to reconfigure | Highly flexible
Working Principle | CSMA/CD (Collision Detection) | CSMA/CA (Collision Avoidance)
Interference / Fluctuations ? | Very Low | High (affected by walls, devices, etc.)
Installation Activity | Cumbersome; labor-intensive | Easy; minimal labor
Installation Time | Long (due to cabling, physical setup) | Quick deployment
Connection Type | Usually Dedicated | Shared
Installation Cost | High (cables, labor, devices) | Low
Maintenance Cost | High | Low
Related Equipment | Router, Switch, Hub | Wireless Router, Access Point
Key Benefits | High speed, stable, secure, noise-immune | Cable-free, mobile-friendly, easy to install

## Slide 13: Wired Vs. Wireless Communication
Parameter | Wired Network | Wireless Network
Communication Medium | Copper, Fiber optic | Air (Radio Waves)
Standard | IEEE 802.3 (Ethernet) | IEEE 802.11 family (Wi-Fi)
Mobility & Roaming | Limited | High
Security | High (less vulnerable to attacks) | Lower (prone to eavesdropping/hacking)
Speed / Bandwidth | Very High (up to 1 Gbps or more) | Moderate to Low
Delay (Latency) | Low | High
Reliability | Very High | Less reliable
Flexibility to Change | Rigid setup, hard to reconfigure | Highly flexible
Working Principle | CSMA/CD (Collision Detection) | CSMA/CA (Collision Avoidance)
Interference / Fluctuations | Very Low | High (affected by walls, devices, etc.)
Installation Activity ? | Cumbersome; labor-intensive | Easy; minimal labor
Installation Time ? | Long (due to cabling, physical setup) | Quick deployment
Connection Type ? | Usually Dedicated | Shared
Installation Cost | High (cables, labor, devices) | Low
Maintenance Cost | High | Low
Related Equipment | Router, Switch, Hub | Wireless Router, Access Point
Key Benefits | High speed, stable, secure, noise-immune | Cable-free, mobile-friendly, easy to install

## Slide 14: Wired Vs. Wireless Communication
Parameter | Wired Network | Wireless Network
Communication Medium | Copper, Fiber optic | Air (Radio Waves)
Standard | IEEE 802.3 (Ethernet) | IEEE 802.11 family (Wi-Fi)
Mobility & Roaming | Limited | High
Security | High (less vulnerable to attacks) | Lower (prone to eavesdropping/hacking)
Speed / Bandwidth | Very High (up to 1 Gbps or more) | Moderate to Low
Delay (Latency) | Low | High
Reliability | Very High | Less reliable
Flexibility to Change | Rigid setup, hard to reconfigure | Highly flexible
Working Principle | CSMA/CD (Collision Detection) | CSMA/CA (Collision Avoidance)
Interference / Fluctuations | Very Low | High (affected by walls, devices, etc.)
Installation Activity | Cumbersome; labor-intensive | Easy; minimal labor
Installation Time | Long (due to cabling, physical setup) | Quick deployment
Connection Type | Usually Dedicated | Shared
Installation Cost ? | High (cables, labor, devices) | Low
Maintenance Cost ? | High | Low
Related Equipment ? | Router, Switch, Hub | Wireless Router, Access Point
Key Benefits | High speed, stable, secure, noise-immune | Cable-free, mobile-friendly, easy to install

## Slide 15: Wired Vs. Wireless Communication
Parameter | Wired Network | Wireless Network
Communication Medium | Copper, Fiber optic | Air (Radio Waves)
Standard | IEEE 802.3 (Ethernet) | IEEE 802.11 family (Wi-Fi)
Mobility & Roaming | Limited | High
Security | High (less vulnerable to attacks) | Lower (prone to eavesdropping/hacking)
Speed / Bandwidth | Very High (up to 1 Gbps or more) | Moderate to Low
Delay (Latency) | Low | High
Reliability | Very High | Less reliable
Flexibility to Change | Rigid setup, hard to reconfigure | Highly flexible
Working Principle | CSMA/CD (Collision Detection) | CSMA/CA (Collision Avoidance)
Interference / Fluctuations | Very Low | High (affected by walls, devices, etc.)
Installation Activity | Cumbersome; labor-intensive | Easy; minimal labor
Installation Time | Long (due to cabling, physical setup) | Quick deployment
Connection Type | Usually Dedicated | Shared
Installation Cost | High (cables, labor, devices) | Low
Maintenance Cost | High | Low
Related Equipment | Router, Switch, Hub | Wireless Router, Access Point
Key Benefits ? | High speed, stable, secure, noise-immune | Cable-free, mobile-friendly, easy to install

## Slide 16: Wired Vs. Wireless Communication
Parameter | Wired Network | Wireless Network
Communication Medium | Copper, Fiber optic | Air (Radio Waves)
Standard | IEEE 802.3 (Ethernet) | IEEE 802.11 family (Wi-Fi)
Mobility & Roaming | Limited | High
Security | High (less vulnerable to attacks) | Lower (prone to eavesdropping/hacking)
Speed / Bandwidth | Very High (up to 1 Gbps or more) | Moderate to Low
Delay (Latency) | Low | High
Reliability | Very High | Less reliable
Flexibility to Change | Rigid setup, hard to reconfigure | Highly flexible
Working Principle | CSMA/CD (Collision Detection) | CSMA/CA (Collision Avoidance)
Interference / Fluctuations | Very Low | High (affected by walls, devices, etc.)
Installation Activity | Cumbersome; labor-intensive | Easy; minimal labor
Installation Time | Long (due to cabling, physical setup) | Quick deployment
Connection Type | Usually Dedicated | Shared
Installation Cost | High (cables, labor, devices) | Low
Maintenance Cost | High | Low
Related Equipment | Router, Switch, Hub | Wireless Router, Access Point
Key Benefits | High speed, stable, secure, noise-immune | Cable-free, mobile-friendly, easy to install

## Slide 17: Wired Vs. Wireless Communication
Parameter | Wired Network | Wireless Network
Communication Medium | Copper, Fiber optic | Air (Radio Waves)
Standard | IEEE 802.3 (Ethernet) | IEEE 802.11 family (Wi-Fi)
Mobility & Roaming | Limited | High
Security | High (less vulnerable to attacks) | Lower (prone to eavesdropping/hacking)
Speed / Bandwidth | Very High (up to 1 Gbps or more) | Moderate to Low
Delay (Latency) | Low | High
Reliability | Very High | Less reliable
Flexibility to Change | Rigid setup, hard to reconfigure | Highly flexible
Working Principle | CSMA/CD (Collision Detection) | CSMA/CA (Collision Avoidance)
Interference / Fluctuations | Very Low | High (affected by walls, devices, etc.)
Installation Activity | Cumbersome; labor-intensive | Easy; minimal labor
Installation Time | Long (due to cabling, physical setup) | Quick deployment
Connection Type | Usually Dedicated | Shared
Installation Cost | High (cables, labor, devices) | Low
Maintenance Cost | High | Low
Related Equipment | Router, Switch, Hub | Wireless Router, Access Point
Key Benefits | High speed, stable, secure, noise-immune | Cable-free, mobile-friendly, easy to install
How to Address These Limitations of Wireless Networks
to Boost Communication Performance?

## Slide 18: What Are the Limitations of Wireless Communications?
Power Constraints | Battery-operated devices must optimize transmission to save power.
Limitation | Description
Susceptible to Interference | From other wireless devices or physical obstacles (walls, appliances).
Signal Attenuation & Fading | Signals weaken over distance and vary due to multipath propagation.
Bandwidth Limitations | Shared medium leads to congestion and reduced throughput.
Security Vulnerabilities | Easier to intercept or attack (e.g., spoofing, eavesdropping).
Mobility-Induced Handover Delays | Switching between access points can cause latency or packet loss.

## Slide 19: Embracing Wireless: Key Motivations
Advantages
Eliminates the need for physical cabling in difficult or remote areas
Enables user mobility and flexible access
Lower installation cost in many environments

## Slide 20
How to Address These Limitations to Boost Communication Performance?
Challenge | Solutions
Interference | Use directional antennas, adaptive frequency selection, and smart AP placement.
Signal Attenuation | Deploy MIMO, repeaters, and mesh networks for better coverage.
Bandwidth Sharing | Cognitive Radio for Spectrum Sharing, Apply QoS (Quality of Service)
Handover Delays | Use fast handoff techniques and mobile IP support for seamless mobility.
Power Efficiency | Use energy-aware MAC protocols and sleep cycles.
Security Threats | Implement WPA3, VPNs, firewalls, and regular firmware updates.

## Slide 21
Wireless Wireless links characteristics

## Slide 22
How does signal propagate ?
How much attenuation take place ?
How does signal look like at the receiver ?
Tx
Rx
Understanding Wireless Links

## Slide 23: Wireless Link Characteristics
Differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
Wireless is a broadcast medium!
space
Signal Strength

## Slide 24: Wireless Link Characteristics
Differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors, microwaves) interfere as well
Wireless is a broadcast medium!
space
Signal Strength

## Slide 25: Wireless Link Characteristics
Differences from wired link ….
  multipath propagation (fading): radio signal reflects off objects or ground, arriving at destination at slightly different times
    Reflection
    Diffraction
    Scattering
Wireless is a broadcast medium!

## Slide 26: Wireless Link Characteristics
Differences from wired link ….
  decreased signal strength:
  interference from other sources:
  multipath propagation (fading):
    Reflection
    Diffraction
    Scattering
Wireless is a broadcast medium!
…. make communication across (even a point to point) wireless link much more “difficult”
space
Signal Strength

## Slide 27: Impact of Multipath Propagation
Direct signal
Reflected signal
Received signal

## Slide 28: Wireless Link Characteristics– Fading
Channel characteristics change over time and location
  e.g., movement of sender, receiver and/or scatters
 quick changes in the power received (short term/fast fading)
 slow changes in the average power received (long term/slow fading)
short term fading
long term
fading
t
power
Notes: Fast fading: usually observed over distances of about half a wavelength. For VHF and UHF, a vehicle traveling at 30 miles per hour can pass through several fast fades in a second
Slow fading: movement over distances large enough to produce gross variations in the overall path

## Slide 29: Wireless Link Characteristics– Fading
1 W
d2
10 W
source
d1
1 mW
10-3
101
10-6
Power
dB = 10 log (----)
P1
P2
Path loss from source to d2 = 70dB
1,000 times
40 dB
30 dB
10,000 times
Where:
P1 ​ = Transmitted Power
P2 ​ = Received Power
Sample Example
Path loss in decibel,

## Slide 30: Wireless Link Characteristics– Fading
  To convert power from milliwatts (mW) to decibel-milliwatts (dBm), use the formula:
  P (dBm) = 10 · log10(P (mW))
  If,
  Transmitted Signal Power: Ptx decibel-milliwatts (dBm)
  Receiver Sensitivity: Prx decibel-milliwatts (dBm)
  Maximum Tolerable Path Loss = Ptx (dBm) − Prx (dBm)

## Slide 31: Typical Picture
slow fading
fast fading
path loss
log (distance)
Received
Signal
Power
(dBm)
Notes: Pt = PrGtGr (λ/4pR)^2

## Slide 32: Attenuation
Strength of signal falls off with distance over transmission medium
Attenuation factors for unguided media:
  Received signal must have sufficient strength so that circuitry in the receiver can interpret the signal
  Signal must maintain a level sufficiently higher than noise to be received without error
  Attenuation is greater at higher frequencies, causing distortion
Approach: amplifiers that strengthen higher frequencies

## Slide 33: Attenuation: Propagation & Range

## Slide 34: Signal Propagation Ranges
distance
sender
transmission
detection
interference
Transmission range
  communication possible
  low error rate
Detection range
  detection of the signal possible
  no communication possible
Interference range
  signal may not be detected
  signal adds to the background noise
Notes: These ranges are not circular in the real world.

## Slide 35: Signal, Noise, and Interference
Signal (S)
Noise (N)
  Includes thermal noise and background radiation
Interference (I)
  Signals from other transmitting sources
SINR = S/(N+I) (sometimes also denoted as SNR)
Large SINR = easier to extract signal from noise

## Slide 36: dB and Power conversion
dB
  Denote the difference between two power levels
  (P2/P1)[dB] = 10 * log10 (P2/P1)
  P2/P1 = 10^(A/10)
  Example 1: P2 = 10 P1, P2/P1=10dB
  Example 2: P2/P1 = 33dB, P2 = 2000 P1
dBm and dBW
  Denote the power level relative to 1 mW or 1 W
  P[dBm] = 10*log10(P/1mW)
  P[dBW] = 10*log10(P/1W)
  Example: P = 0.001mW = -30dBm, P = 100W = 20dBW
10dB: factor of 10
3dB: factor of 2

## Slide 37: Wireless Link Characteristics
SNR: signal-to-noise ratio
  larger SNR – easier to extract signal from noise
SNR versus BER tradeoffs
  given physical layer: increase power -> increase SNR->decrease BER
  given SNR: choose physical layer that meets BER requirement, giving highest throughput
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4

## Slide 38
Rate Adaptation
base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, SNR varies
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
10
20
30
40
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
operating point
1. SNR decreases, BER increase as node moves away from base station
2. When BER becomes too high, switch to lower transmission rate but with lower BER

## Slide 39: Understanding Wireless Communication: Barriers

## Slide 40: Wireless is less reliable
In wired networks, link bit error rate is 10-12 and less
Wireless networks are far from that target
– Bit error rates of 10-6 and above are common!
Why?
Alice
Bob

## Slide 41: Wireless is a shared medium
Wired networks:
Alice and Bob’s conversation is independent of Cathy and Eve’s conversation
Wireless networks:
Close by wireless conversations share the same wireless medium
Alice
Bob
Cathy
Eve

## Slide 42: Wireless Links: High Bit Error Rate
“Wireless communication often faces disruptions from the environment, causing more errors in the received data, known as a high Bit Error Rate (BER).”
Factors Contributing to High BER::
Signal Attenuation:
  Signal gets weaker with distance or obstacles, making it harder to receive clearly.
Noise and Interference:
  Other electronic signals mix with the intended one, causing data errors.
Multipath Fading & Environmental Obstructions:
  Reflected signals arrive at different times, distorting the original message.
Doppler Shift (Mobility):
  Movement causes frequency changes, making signal decoding difficult.
Broadcast Limitations at Wireless Links

## Slide 43: Dealing With Bit Errors
Wireless vs. wired links
  Wired: most loss is due to congestion
  Wireless: higher, time-varying bit-error ate
Dealing with high bit-error rates
  Sender could increase transmission power
    Requires more energy (bad for battery-powered hosts)
    Creates more interference with other senders
  Stronger error detection and recovery
    More powerful error detection codes
    Link-layer retransmission of corrupted frames

## Slide 44: 1. Signal Attenuation

## Slide 45: 1. Signal Attenuation
Signal Attenuation:: Decreasing signal strength
  Disperses as it travels greater distance
  Attenuates as it passes through matter

## Slide 46: 1.Signal Attenuation:: High BER
Decreasing signal strength
  Disperses as it travels greater distance
  Attenuates as it passes through matter
    Metal particles present in air
    Noice and interference
Lower signal-to-noise ratio (SNR) increases the probability of bit errors

## Slide 47: 1.Signal Attenuation
Received Signal Strength:: Wired vs Wireless
A
B
C
A’s signal
strength
space
C’s signal
strength
Received Signal Strength in Wireless Networks
Received Signal Strength in Wired Networks

## Slide 48: 1.Signal Attenuation
Received Signal Strength in Wired Networks
Reason: Minimal Signal Loss in Wired
Signals travel through guided media like copper or fiber.
These media shield signals from external interference and minimize attenuation.
Losses due to resistance or cable imperfections are very small over short-to-moderate distances.

## Slide 49: 1.Signal Attenuation
Reason: Higher Signal Loss in Wireless
In wireless networks, RSS drops rapidly with distance due to:
Path loss
Obstacles
Noise and interference
A
B
C
A’s signal
strength
space
C’s signal
strength
Received Signal Strength in Wireless Networks

## Slide 50: 1.Signal Attenuation
The higher frequencies will
usually encounter more “loss”
in “real world” situations

## Slide 51: 2. Noise and Interference

## Slide 52: Categories of Noise
Thermal Noise
Intermodulation noise
  Occurs when signals at different frequencies mix and produce additional unwanted signals.
Crosstalk
  Unwanted signal leakage between adjacent cables or channels.
Impulse Noise
2. Noise and Interference
Caused by the random motion of electrons in a conductor.
Present in all electronic devices and transmission media.
Increases with temperature; affects all frequencies uniformly.
Sudden, short-duration high-energy spikes.
Caused by lightning, switching equipment, or power line disturbances.
Particularly harmful to digital communication; can corrupt multiple bits at once.

## Slide 53: 2. Noise and Interference
Interference from other sources
  Radio sources in same frequency band
  E.g., 2.4 GHz wireless phone interferes with 802.11b wireless LAN
  Electromagnetic noise (e.g., microwave oven)

## Slide 54: EM Spectrum

Propagation characteristics are different in each frequency band
UV
1 MHz
1 kHz
1 GHz
1 THz
1 PHz
1 EHz
infrared
visible
X rays
Gamma rays
LF
HF
VHF
UHF
SHF
EHF
MF
AM radio
S/W radio
FM radio
TV
TV
cellular

902 – 928 Mhz
2.4 – 2.4835 Ghz
5.725 – 5.785 Ghz
ISM band

30kHz
300kHz
3MHz
30MHz
300MHz
30GHz
300GHz
10km
1km
100m
10m
1m
10cm
1cm
100mm
3GHz

## Slide 55: EM Spectrum:: ISM Band
ISM Band (Industrial, Scientific, and Medical Band)
Key Features
License-free usage (no regulatory approval needed, with power limits).
Common in Wi-Fi, Bluetooth, RFID, microwave ovens, and cordless phones.
Operates under power and interference constraints to coexist with other users.
Frequency Band | Common Uses
433 MHz | RFID, remote controls (Europe)
868 MHz / 915 MHz | IoT devices, Zigbee, LPWAN
2.4 GHz | Wi-Fi (802.11b/g/n), Bluetooth, Microwave ovens
5.8 GHz | Wi-Fi (802.11a/n/ac), radar, ISM devices
  This can cause interference, especially between Wi-Fi and microwave ovens.
  Modern Wi-Fi devices often switch to 5 GHz or 6 GHz to avoid congestion.

## Slide 56: 2.Noise and Interference:: High BER
How Noise & Interference Increase Bit Error Rate (BER)
Noise (thermal, impulse) distorts the signal, making it hard to detect correct bits.
Interference from nearby devices overlaps signals, causing bit confusion.
Low SNR reduces the receiver’s ability to distinguish between 0s and 1s.

## Slide 57: 3. Multipath Fading & Environmental Obstructions

## Slide 58: The Cluttered World of Radio Waves
walls
hallways
windows
trees
vehicles
rain
hills
girders

## Slide 59: 3.Multipath Fading & Environmental Obstructions: High BER
Multi-path propagation
  Electromagnetic waves reflect off objects
  Taking many paths of different lengths
  Causing blurring of signal at the receiver
  Multipath fading causes signal distortion and delays, increasing errors (BER).
receiver
transmitter

## Slide 60: 3.Multipath Fading & Environmental Obstructions: High BER
Three basic propagation mechanisms
Propagation effects depend on not only on the specific portion of spectrum used for transmission, but also on the bandwidth (or spectral occupancy) of the signal being transmitted
Spatial separation of Tx-Rx
Reflection
λ << D
Diffraction
λ  D
Scattering
λ >> D

## Slide 61: 3.Multipath Fading & Environmental Obstructions: High BER

## Slide 62: 4. Doppler Shift (Mobility):

## Slide 63: 4.Doppler Shift (Mobility):

## Slide 64: 4.Doppler Shift (Mobility): High BER
Doppler Shift causes frequency changes in the received signal due to relative motion between transmitter and receiver.
This leads to carrier frequency offset and loss of synchronization at the receiver.
It also increases channel variation rate, making the channel time-varying and unpredictable.
As a result, symbols may be misinterpreted, especially in high-speed mobility scenarios.
Impact
→ Distorted signal → Synchronization errors → Higher BER

## Slide 65: 5. Broadcast Limitations at Wireless Links

## Slide 66: 5.Wireless Links: Broadcast Limitations
Wired broadcast links
  E.g., Ethernet bridging, in wired LANs
  All nodes receive transmissions from all other nodes
Wireless broadcast: hidden terminal problem
A
B
C
A and B hear each other
B and C hear each other
But, A and C do not
So, A and C are unaware
of their interference at B.

## Slide 67: 5.Wireless Links: Broadcast Limitations
Wired broadcast links
  E.g., Ethernet bridging, in wired LANs
  All nodes receive transmissions from all other nodes
Wireless broadcast: fading over distance
A
B
C
A’s signal
strength
space
C’s signal
strength
A and B hear each other
B and C hear each other
But, A and C do not
So, A and C are unaware
of their interference at B.

## Slide 68: 5.Wireless Links: Broadcast Limitations
Why is this a problem in wireless networks?
A
B
C
A’s signal
strength
space
C’s signal
strength
A
B
C

## Slide 69: 5.Wireless Links: Broadcast Limitations
Why is it NOT a problem in wired networks?
In wired networks, like Ethernet:
  All nodes are also connected to a shared medium (the wire).
  Every device can “hear” all transmissions with acceptable received Signal Strength, so they avoid sending at the same time.
  (CSMA/CD) Collision Detection works well because all signals are detectable.
A
B
C

## Slide 70: 5.Wireless Links: Broadcast Limitations:: High BER
A
B
C
A’s signal
strength
space
C’s signal
strength
Network Type | Can all devices sense each other? | Hidden Terminal Problem?
Wired | ✅ Yes | ❌ No
Wireless | ❌ Not always | ✅ Yes
Impact
→ Undetected collisions at receiver → Corrupted data → Increased BER

## Slide 71: Understanding Wireless Communication: Needs, Barriers, and Design Adaptations

## Slide 72: Understanding Wireless Communication: Needs

## Slide 73: Examples of Communication Requirements
bit error probability: < 0.1 % delay: < 100 ms data rate: 10-15 kbit/s
bit error probability: < 10-9 delay: < 1 day data rate: irrelevant
bit error probability: < 10-5 delay: < seconds data rate: < 80 Mbit/s
Cell phones:
E-mailing:
Mobile broadband:

## Slide 74: Multimedia Requirements
Voice
Video
Data
Delay
Packet Loss
BER
Data Rate
Traffic
<100ms
-
<100ms
<1%
0
<1%
10-3
10-6
10-6
8-32 Kbps
1-100 Mbps
1-20 Mbps
Continuous
Bursty
Continuous
One-size-fits-all protocols and design do not work well
Wired networks use this approach, with poor results

## Slide 75: Understanding Wireless Communication: Design Adaptations

## Slide 76: Possible Design Goals
Maximize the transmission rate
Minimize the probability of error
Minimize the required power
Minimize the required system bandwidth
Maximize system utilization
Minimize system complexity
Minimize communication delay
Some of these goals are in conflict with each other!

## Slide 77: Evolution of Current Systems
Recent past
  2G Cellular: ~30-70 Kbps.
  WLANs: ~10 Mbps.
  3G Cellular: ~300 Kbps.
  WLANs: ~70 Mbps.
Technology Enhancements
  Hardware: Better batteries. Better circuits/processors.
  Link: Antennas, modulation, coding, adaptivity, DSP, BW.
  Network: Dynamic resource allocation. Mobility support.
  Application: Soft and adaptive QoS.

## Slide 78: Design Challenges
Wireless channels are a difficult and capacity-limited broadcast communications medium
Traffic patterns, user locations, and network conditions are constantly changing
Applications are heterogeneous with hard constraints that must be met by the network
Energy and delay constraints change design principles across all layers of the protocol stack

## Slide 79: OSI Model
Computer Science
Electrical Engineering
PHY
Link
Network
Application
Spectrum
Notes: Knowledge across layers is necessary to make informed decision.

## Slide 80: Crosslayer Design
Hardware
Link
Access
Network
Application
Delay Constraints
Rate Constraints
Energy Constraints
Adapt across design layers
Reduce uncertainty through scheduling
Provide robustness via diversity